## Slide 1: Computer Architecture Tutorial 2
LOGOS LAB
2017/03/28

## Slide 2: Outline
Project 1 – Issues
  Submission issue
  Demo day
Project 2 – Pipeline
  Concept
  Input & Output
  Submission

## Slide 3: Project 1 – Issues

## Slide 4: Submission issue
Fairness
Your simulator should “make” on our server.
Your output should be same as golden simulator output.
  We don’t accept more command options.

## Slide 5: NOP instruction
Specify “sll $0, $0, 0” to “NOP”.
  0x00000000 is an example.
  In “sll”, $rs is don’t care number.

## Slide 6: Demo day
Date: 4/07(Fri.)
Time: 15 mins/person
Place: General Building II(綜二) 737、738
Content: makefile, git, gdb, Q&A

## Slide 7: Project 2 - Pipeline

## Slide 8: Single Cycle Data Path
Low design complexity
Poor throughput

## Slide 9: Pipeline
IF/ID
ID/EX
EX/DM
DM/WB
More complex design
High throughput

## Slide 10: 5 Pipeline Stages
Independent of instruction type
IF
  instruction fetch
  PC+4
ID
  Read Register File
  Sign extension
  Control unit decode
  Hazard detect, Branch/Jump detect, Branch
Dependent of instruction type
EX
  ALU
DM
  Access data memory
WB
  Write value to Register File

## Slide 11: Resolving Pipeline Hazards
Data hazard
  Stall
  Forwarding ( appendix C-2 )
    EX/DM to ID
    EX/DM to EX
    DM/WB to EX
Control hazard
  Flush

## Slide 12: Forwarding Paths
IF/ID
ID/EX
EX/DM
DM/WB
EX/DM to ID
EX/DM to EX
DM/WB to EX

## Slide 13: Input & Output
Input: same as project 1
Output:
  snapshot.rpt
    Contents of registers
      whether an instruction is completely executed
    Status of the instruction executing in a pipeline stage
      whether to be stalled in next cycle
      whether to forward in this cycle
  error_dump.rpt
    Different listing order

## Slide 14: Snapshot: Stall
Data hazard

## Slide 15: Snapshot: Forwarding
Data hazard
EX/DM

## Slide 16: Snapshot: Register contents
…

## Slide 17: Snapshot: Flush
error_3

## Slide 18: Test Case Design
Your test case should cover at least one hazard handling.
The number of NOPs and forwarding paths is not limited.
< 500,000 cycles

## Slide 19: Implementation
Initialization: The pipeline is initialized with NOPs in all stages
Termination: after five “halt”s; otherwise invalid

## Slide 20: Implementation
IF/ID
ID/EX
EX/DM
DM/WB
Simulation Order (highly recommended)
  WB  DM  EX  ID  IF
add $3, $1, $4
lw $1, 0($2)
Notes:   Function角度解釋

## Slide 21: Modules
C files
main.c
simulate.c
instruction.c
regfile.c
memory.c
pipereg.c
piperpt.c
hazard.c
Header files
arithmetic.h
simulate.h
instruction.h
regfile.h
memory.h
pipereg.h
piperpt.h
hazard.h

## Slide 22: Submission
Same grading policy as that of project 1
1st Submission: 2017/ 4/ 29
2nd Submission: 2017/ 5/ 06

## Slide 23
Q&A